AMUSE
Astrophysical Multiscale Software Environment
INTRODUCTION TO THE SOFTWARE
Arjen van Elteren

---
Goal
Phyisics:
To create an instrument for performing astrophysical experiments spanning multiple physical domains and a wide range in temporal and spatial scales.
Software:
Combining existing, proven codes into a loosely coupled but consistent software environment, without changing the legace codes (much)!

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Design – overview
Stellar Evolution
Hydrodynamics
Radiative Transfer
Gravity
AMUSE
Combining existing codes
With an extensive support framework
 To provide a generic framework
For doing astrophysical experiments
INPUT
OUTPUT
Compare models
Unit handling
Data conversion
Initial conditions

---
Design – blocks

---
Design – levels

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Code
- Python
- Legacy codes, C/C++, Fortran
- Interface between python and legacy code via MPI
- Organised in directory stucture

---
Directory Structure
- trunk
  - src, source code of the environment and included legacy modules
  - test, source code of all unittesting code and examples
  - support + bin, code for building and testing the software
  - doc, installation documentation, tutorials and reference documentation

---
SRC directory
- Everything in one master package called amuse
- This package is divided in sub-packages
  - legacy, contains all the legacy codes, for each legacy code a sub-package, not divided in physical domains
  - support, code for the unit handling, data model, input/output
  - domain, domain specific definitions of interfaces, attributes and parameters (tentative)

---
TEST directory
- Contains directories for different unit tests, contains examples directory
  - examples, applications using the AMUSE framework
  - legacy_tests, unittests for the legacy codes. Tests of the MPI interfaces and very simple problems (sun and earth for gravitational dynamics)
  - core_tests, tests of the support package (units handling, IO, data model)

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Interfacing Legacy Code
- Based on function/subroutine calls
- Function calls are remote, from python application to legacy code application
- Function calls are over MPI, MPI is used to transfer data from python to the legacy code
- Python interface is defined as a python class, some special syntax needed to specify the remote functions (python decorator @legacy_function)

---
Example
Python Definition
class Interface(LegacyInterface):
  @legacy_function
  def sum():
    function = RemoteFunction()
    function.add_parameter('x', 'd', function.IN)
    function.result_type = 'd'
    return function
C code
double sum(double x, double y) {
return x+y;
}
Python script
x = new Interface()
result = x.sum(10.5, 31.5)
print result

---
MPI – how it works 1
interface
class
defined
during
integration
generic
handling
function
calls
main
event-loop
generated!
legacy
code
existing
or
defined
functions
MPI
method
calls
function
call
python
C++ or Fortran 90

---
MPI – how it works 2
- Every MPI exchange starts with a fixed with header, detailing the following messages and the function to call.
- Parameters are encoded into arrays of a specific type (doubles, floats, integers)
- These arrays are send using MPI's Bcast, Send and Recieve functions

---
MPI – parallel code
- Existing parallel codes can work with this model.
- Communication with legacy code is over a “special” intra-communication channel
- Request message is broadcasted to all sub-processes, result message only from root process

---
MPI – final words
- MPI is also used to start the legacy code (MPI 2 spawn)
- TODO:
  - Events to send back information to the python script (collision partners, diagnostic values)
  - We can send arrays, need also handling to put these arrays directly into the legacy codes (now we use a loop)
  - Use MPI to interact with python classes

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Interface – next level
- Use legacy functions to interact with:
  - parameters, code wide specific settings, usually only changed at the start of a calculation
  - data (attributes of particles or of gridpoints), set the initial conditions, retrieve the latest calculated values
  - evolve, let the legacy code evolve the model
  - diagnostics, get important information about the state of the code (energy, time, ...)
  - services, calculate values based on the model (gravity on a given point)

---
Interface – next level
- All values in a python script have units
  - legacy code only knows about numbers, units are implicit
  - next level combines the numbers with units into values, or strips the units from the values to get the numbers to send to the legacy code
- Legacy codes may know about ids
  - next level connects ids to objects (stars, gas particles) with attributes

---
Interface – next level
- Legacy code knows about current time (or just as much history as is needed for the calculation)
  - next level adds history, i.e. the value of an attribute at a specific model time is stored.
- Legacy code is defined in functions
  - next level definitions are based on interface (data transfer, model update, gravity service)

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Units and Values
- Units are defined in a base system
- Default base system is SI (kg, m, s, K, A, mol, cd)
- Units can be composed of other units (m/s)
- Units can be derived from other units (parsec)
- Another base system is NBODY (G=1)
- Converter to go from nbody to SI and back
- Value is a number combined with a unit
- All operations work on values

---
Units and Values – example
Units
>>> parsec = named('parsec','pc', 3.08568025e16 * m)
>>> kparsec = 1000 * parsec
>>> print kparsec
unit<1000 * parsec>
>>> value1 = 10 | kparsec
>>> print value1
10 1000 * parsec
>>> value2 = 1 | parsec
>>> print value2
1 parsec
>>> value2 + value1
value<10001.0 parsec>
>>> (value2 + value1).in_(kparsec)
value<10.001 1000 * parsec>
>>>
>>> convert = nbody_to_si(1 | MSun, 1 | parsec)
>>> l = 10 | length
>>> l
value<10 nbody length>
>>> convert.to_si(l)
value<3.08568025e+17 m>
>>> convert.to_si(l).in_(parsec)
value<10.0 parsec>

---
Roadmap
Code
Legacy
Interface
Design
Run an Application
Units
Next Level

---
Example Application
from amuse.legacy.bhtree.muse_dynamics_mpi import BHTree
convert_nbody=nbody_system.nbody_to_si(total_mass, 1 | units.parsec)
particles=MakePlummerModel(number_of_stars, convert_nbody).result;
gravity = BHTree(convert_nbody)
gravity.parameters.epsilon_squared = 0.3 | units.parsec ** 2
time = 1 | units.Myr
total_energy_at_t0 = sum(gravity.get_energies(), 0 | units.J)
while time < end_time:
  gravity.evolve_model(time)
  total_energy_at_this_time = sum(gravity.get_energies(), 0 | units.J)
  gravity.update_particles(particles)
- Make python script
- Define imports
- Make stars
- Make instances of interface classes
- Input stars in codes
- Run code and update model

---
Example application
from amuse.legacy.bhtree.muse_dynamics_mpi import BHTree
convert_nbody=nbody_system.nbody_to_si(total_mass, 1 | units.parsec)
particles=MakePlummerModel(number_of_stars, convert_nbody).result;
gravity = BHTree(convert_nbody)
gravity.parameters.epsilon_squared = 0.3 | units.parsec ** 2
time = 1 | units.Myr
total_energy_at_t0 = sum(gravity.get_energies(), 0 | units.J)
while time < end_time:
  gravity.evolve_model(time)
  total_energy_at_this_time = sum(gravity.get_energies(), 0 | units.J)
  gravity.update_particles(particles)